## Slide 2: Lecture 8: Caching
Prof. Seyed Majid Zahedi
https://ece.uwaterloo.ca/~smzahedi

## Slide 3: Outline
Principle of locality
  Temporal locality: Locality in time
  Spatial locality: Locality in space
Cache organizations
  Direct mapped, set associative, fully associative
Major categories of cache misses
  Compulsory, conflict, capacity, coherence
Translation lookaside buffer (TLB): caching applied to address translation
  Cache relatively small number of PTEs
  On TLB miss, page table is traversed

## Slide 4: Caching Concept
Cache is repository for copies that can be accessed more quickly
  Make frequent case fast and infrequent case less dominant
Caching underlies many techniques used today to make computers fast
  We can cache memory locations, address translations, pages, file blocks, file names, network routes, etc…
Only good if
  Frequent case is frequent enough and
  Infrequent case is not too expensive

## Slide 5: Why Bother with Caching?
9% per year
(2X/10 years)
DRAM
1
10
100
1000
Normalized Performance Growth
Time
60% per year
(2X/1.5 year)
CPU
“Moore’s Law”
(really Joy’s Law)
Processor-DRAM Memory Gap (latency)
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-Memory
Performance Gap: (grows 50% / year)

## Slide 6: Why Does Caching Help?
Temporal locality (locality in time):
  Cache recently accessed data items
Spatial locality (locality in space):
  Cache contiguous blocks
Address Space
0
2n-1
Probability
of reference
Notes: In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.

## Slide 7: Some Terminology
Block: group of spatially contiguous and aligned bytes (words)
  Typical sizes are 32B, 64B, 128B
Hit: access cache and find what we want
  Hit time: time to hit (or discover miss)
Miss: access cache and fail to find what we want
  Miss time: time to satisfy miss
  Misses are expensive (take a long time) ⇒ try to avoid them
  But, if they happen, amortize their costs ⇒ bring in more than just specific word you want ⇒ bring in whole block (multiple words)

## Slide 8: Some Terminology (cont.)
Hit rate = num of hits / (num of hits + num of misses)
  Miss rate = 1 – hit rate
  High hit rate means high probability of finding what we want
Average access time = hit rate x hit time + miss rate x (hit time + miss time)
  = hit time + miss rate x miss time
Problem: hard to get low hit time and miss rate in one memory structure
  Large memory structures have low miss rate but high hit time
  Small memory structures have low hit time but high miss rate
Solution: use hierarchy of memory structures

## Slide 9: Memory Hierarchy of Modern Computer Systems
Goal: bring average memory access time close to L1’s
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
Secondary Storage (SSD)
1
10,000,000 (10 ms)
Speed (ns):
10-30
100
0.3
3
100,000 (0.1 ms)
100Bs
Size (bytes):
MiBs
GiBs
TiBs
10KiBs
100KiBs
100GiBs
Compiler
Managed
Hardware
Managed
Software
Managed (by OS)
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).

## Slide 10: Abstract Hierarchy Performance
Avg. memory access time = Avg-timeM1
= Hit-timeM1 + (Miss-ratioM1 x Miss-timeM1)
= Hit-timeM1 + (Miss-ratioM1 x Avg-timeM2)
= Hit-timeM1 + (Miss-ratioM1 x (Hit-timeM2 + (Miss-ratioM2 x Miss-timeM2)))
= Hit-timeM1 + (Miss-ratioM1 x (Hit-timeM2 + (Miss-ratioM2 x Avg-timeM3)))
= …
Miss time at level X = Average access time at level X + 1
M1
M2
M3
M4
CPU

## Slide 11: Caching Questions
8-byte cache, 32-byte memory, 1 block = 1 byte
Assume CPU accesses 01100
How do you know whether byte @ 01100 is cached?
Cache
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
000
001
010
011
100
101
110
111
Physical Memory
(01100)

## Slide 12: Caching Questions (cont.)
8-byte cache, 32-byte memory, 1 block = 1 byte
Assume CPU accesses 01100
How do you know whether byte @ 01100 is cached?
If not, at which location in cache should it be placed?
Cache
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
000
001
010
011
100
101
110
111
Physical Memory
(01100)

## Slide 13: Caching Questions (cont.)
8-byte cache, 32-byte memory, 1 block = 1 byte
Assume CPU accesses 01100
How do you know whether byte @ 01100 is cached?
If not, at which location in cache should it be placed?
If cache is full, which cached byte should be evicted?
Cache
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
000
001
010
011
100
101
110
111
Physical Memory

## Slide 14: Where to Put Blocks in Cache?
Divide cache into disjoint sets of blocks
  There is 1-to-1 mapping from block address to set
M-way set-associative cache: each set holds M number of blocks
  E.g., 4 blocks per set ⇒ 4-way set-associative cache
Fully-associative cache: whole cache has just one set
  + Most flexible
  − Longest access latency
Direct-mapped cache: each set has one block (= 1-way set-associative)
  + Least flexible
  − Shortest access latency

## Slide 15: Example: Direct-mapped Cache
Each byte (block) in physical memory is cached to single cache location
  Least significant bits of address (last 3 bits) index cache
  (00100),(01100),(10100),(11100) cached to 100
How do we know which byte is cached?
  Tag each byte with the most significant two bits
Cache
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
000
001
010
011
100
101
110
111
Physical Memory
Tag
01

## Slide 16: Example: Fully-associative Cache
Each byte (block) can be stored at any location in cache
How do you know which byte is cached?
  Tag entire address of cached byte
Cache
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
000
001
010
011
100
101
110
111
Physical Memory
Tag
01100

## Slide 17: Where to Put Blocks in Cache? (cont.)
Example: where is block 12 placed in 8-block cache?
32-Block Address Space
Block address
0
0
0
1
0
2
0
3
0
4
0
5
0
6
0
7
0
8
0
9
1
0
1
1
1
2
1
3
1
4
1
5
1
6
1
7
1
8
1
9
2
0
2
1
2
2
2
3
2
4
2
5
2
6
2
7
2
8
2
9
3
0
3
1
Block number
Direct mapped
Block 12 can go only into block 4 (12 mod 8)
0
1
2
3
4
5
6
7
Fully associative
Block 12 can go anywhere
0
1
2
3
4
5
6
7
2-way set-associative
Block 12 can go anywhere in set 0 (12 mod 4)
0
1
2
3
0
1
2
3
Set 1
Set 2
01
100
Tag
Index
011
00
Tag
Index
01100
Tag
Index

## Slide 18: How is Block Found in Cache?
Byte select field used to select data within block
  Offset of byte in block
Cache index used to lookup candidate blocks in cache
  Index identifies set
Cache tag used to identify actual copy among candidate blocks
  If no candidate matches, then declare cache miss
Byte Select
Cache Index
Cache Tag
Memory address

## Slide 19: Direct Mapped Cache
0x50
Direct mapped 2N byte cache with block size of 2M bytes
  Uppermost (32 - N) bits of address are cache tag
  Lowest M bits are byte select, rest are cash index
Example: 1KiB direct mapped cache with 32B blocks
  Log232 = 5 bits for byte select, 32 – Log21024 = 22 bits for cache tag
  32 – 5 – 22 = 5 bits for cache index
Example: 0x50
0x00
0x01
Byte Select
Cache Index
Cache Tag
0
4
31
9
Memory address
31
:
Valid Bit
Cache Tag
Cache Data
0
1
2
3
:
B0
B1
B31
:
B33
B63
B992
B1023
:
:
B32
:
Cache structure
1

## Slide 20: Set-Associative Cache
=
=
2K-way set-associative 2N byte cache with block size of 2M bytes
  Lowest M bits for byte select, (32 – N + K) bits for cache tag, rest for cache index
  2K direct mapped caches operates in parallel
Previous example, now with 2-way set-associativity
  Cache Index selects “set” from cache, there are 16 sets ⇒ 4 bits for index
Cache Structure
:
Valid Bit
Cache Tag
Cache Data
:
:
Cache Block 0
Cache Block 1
Cache Block 31
Byte Select
Cache Index
Cache Tag
0
4
31
8
Memory address
31
:
Valid Bit
Cache Tag
Cache Data
0
1
2
3
:
:
Cache Block 0
Cache Block 1
Cache Block 31
Cache Block
0
1
selc1
selc0
OR
Hit

## Slide 21: Fully Associative Cache
Every cache block can hold any memory block
  Address does not include cache index
  Compare cache tags of all cache blocks in parallel
Previous example now with fully associative cache
=
=
:
=
Byte Select
Cache Tag
0
4
31
Memory address
Cache Structure
31
:
Valid Bit
Cache Tag
Cache Data
0
1
2
3
:
B0
B1
B31
:
B33
B63
B992
B1023
:
:
B32
:
Hit

## Slide 22: Effective Cache
Consider 2-MiB, 8-way-set-associative cache and 4KiB physical pages
Suppose HW uses low-order bits of physical address to index cache
Suppose process A is allocated physical pages that are separated by 256KiB
How much cache capacity process A can effectively use?
  Bytes in memory that are separated by 256KiB are mapped to same cache set
  A will only be able to use 32KiB (4KiB pages times 8-way set associativity)
  A can only use less than 2% of cache!

## Slide 23: Page Coloring
Physical pages are given colors
Pages with same color will be mapped to the same set in cache
  In above example, there will be 64 different colors (256KiB divided by 4KiB pages)
Kernel maps sequential virtual pages to physical pages with different colors
  Sequential pages in virtual memory do not contend for the same cache set
en.wikipedia.org

## Slide 24: Possible Sources of Cache Misses
Compulsory (cold)
  Cache hasn’t seen this block before (start or migration of process)
  “Cold” fact of life: not whole lot you can do about it
Capacity
  Cache cannot contain all blocks accessed by program
  Solution: increase cache size
Conflict (collision)
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity (no conflict misses in fully associative cache)
Coherence (invalidation)
  Other process (e.g., I/O) updates memory

## Slide 25: Replaced Policy on Cache Miss?
Easy for direct mapped: only one possibility
For set associative or fully associative
  Random
  Least Recently Used (LRU, more on this later)

## Slide 26: What Happens on Write?
Write-through: write to both cache and lower-level memory
  + Read misses cannot result in writes
  − Processor held up on writes unless writes are buffered
Write-back: write only to cache
  Modified cache block is marked dirty
  On replacement, dirty block is written to lower-level memory
  + Repeated writes are not sent to DRAM
  + Processor not held up on writes
  − More complex
  − Read miss may require writeback of dirty data

## Slide 27: Caching Address Translations
Cannot afford to translate on every access
  At least five DRAM accesses per actual DRAM access
  Or: perhaps I/O if page table partially resides on disk!
  Even worse, what if we use caches to make memory access faster than DRAM access?

## Slide 28: Recall: Memory Hierarchy
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
Secondary Storage (SSD)
1
10,000,000 (10 ms)
Speed (ns):
10-30
100
0.3
3
100,000 (0.1 ms)
100Bs
Size (bytes):
MiBs
GiBs
TiBs
10KiBs
100KiBs
100GiBs
Page table lives here (perhaps cached)
PT
Address Translation needs to occur here
Compiler
Managed
Hardware
Managed
Software
Managed (by OS)
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).

## Slide 29: Translation Lookaside Buffer (TLB)
Main idea: cache recent virtual page number to physical page number translations
TLB hit provides physical address without reading any of page tables!
  Caches end-to-end result
  Even if translation involved multiple levels
Does page locality exist?
  Instruction accesses: sequential accesses ⇒ Frequent accesses to the same page ⇒ Yes!
  Stack accesses: definite locality of reference ⇒ Yes!
  Data accesses: less page locality, but still some ⇒ Yes, so so!

## Slide 30: TLB: Caching Applied to Address Translation
CPU
TLB
Page Tables
Physical Memory
Virtual Address
Miss
Invalid
Raise Exception
+
Offset
Hit
Physical Address
Data
Cache
Valid

## Slide 31: TLB Consistency with PTEs
If PTE permission is reduced: TLB entry should be invalidated
  Early computers discarded entire TLB
  Modern architectures allow removal of individual entries
If PTE permission is added: nothing needs to be done
  E.g., changing invalid to read-only or read-only to read-write
  Any reference would cause exception, OS removes TLB entry
If PTE is invalidated: TLB entry should be invalidated too
  E.g., swapping out page from memory to disk (more on this later)

## Slide 32: Accessed and Dirty Bits
TLB entries generally don’t have accessed bit
  If address is cached in TLB, it already should have been accessed
  Page-table walk sets accessed bit of PTE on TLB miss
TLB entries do have dirty bit
  When write misses in TLB, page-table walk sets dirty bit in PTE and TLB
  Even when write hits in TLB, page-table walk is necessary to set dirty bit if it isn’t set
  If dirty bit is set in TLB, no page-table walk is necessary (saving memory bandwidth)
Do we really need dirty bit in PTE and TLB?
  No! OS can emulate it (e.g., BSD Unix)
  Initially, mark all pages as read-only
  On write, trap to OS, set software dirty bit, and mark page as read-write
Do we really need access bit in PTE?
  No! OS can emulate it
  Initially, mark all pages as invalid
  On read, trap to OS (invalid), set software access bit, and mark page read-only
  On write, trap to OS (invalid or read-only), set software access and dirty bits, mark page read-write

## Slide 33: Homonyms
Definition: single virtual address mapped to different physical addresses
Problem: TLB entries are invalid after context switching to another process
Solution 1: invalidate all TLB entries
  + Simple
  − Expensive (what if switching frequently between processes)
Solution 2: tag each TLB entry with process-context identifier (PCID)
  + Less expensive
  − Needs extra hardware

## Slide 34: TLB Shootdown
If processor1 updates process 0’s PTE for page 0x53, then it should
  Remove old entry from its TLB
  Send inter-processor interrupt to other processors telling them to remove their old entries
Shootdown is complete once all processors verify that their old entry is removed
TLB shootdown overhead increases linearly with number of processors

## Slide 35: What Happens on TLB Miss?
Hardware-traversed page tables
  On TLB miss, hardware walks through current page tables to fill TLB (could be multiple levels)
    Valid PTE: Hardware fills TLB and processor never notices
    Invalid PTE: CPU raises page fault ⇒ Kernel decides what to do next
Software-traversed page tables
  On TLB miss, CPU raises TLB fault
  Kernel walks through page table(s) to find PTE
    Valid PTE: Fills TLB and returns from fault
    Invalid, internally calls page fault handler

## Slide 36: TLB Fault and Page Fault Exceptions
Unlike interrupts, exceptions are synchronous, caused by particular instruction
  E.g., TLB fault or page fault, divide by zero
In general, faulting instruction needs to be restarted after exception is handled
Side effects of faulting instruction need to be undone
  Example: push 10
    What if page fault occurs when write to stack pointer?
    Was sp incremented before or after page fault?
Partially executed instructions should also be undone in out-of-order execution
  Example 1: mul r1, r2, r3 bne r1, r4, loop ld r4,(r5)
    What if it take many cycles to see if r1 = r4, but load has already caused page fault?
  Example 2: div r1, r2, r3 ld r3, (r4)
    What if it takes many cycles to discover divide-by-zero, but load has already caused page fault?

## Slide 37: Precise Exceptions
Instructions retire when their results become visible in architectural state
  E.g., processor registers, memory, etc.
  Architectural state ≠ micro-architectural state (e.g., caches)
To implement precise exceptions, instructions should retire in program’s sequential order
  Execution could still be out-of-order
Exception should only be raised when faulting instruction tries to retire
  All instructions before faulting instruction should have already retired
When exception is raised, architectural state should be preserved
  Faulting instruction and all following instructions act as if they have not even started
Faulting
Inst 1
User
Fetch Page/Load TLB
Faulting
Inst 1
Faulting
Inst 2
OS
Page Fault
Faulting
Inst 2
Fetch page/Load TLB
Page Fault

## Slide 38: Improve Efficiency Even More!
TLB improves performance by caching recent translations
How to improve performance even more?
  Multi-level TLBs
What is the cost of first-level TLB miss?
  Second-level TLB lookup
What is the cost of second-level TLB miss?
  x86: 2-4 level page table walk

## Slide 39: Virtually-addressed Cache
Too slow to access TLB before looking up address in memory
Instead, add virtually-addressed cache (virtual cache)
In parallel, access TLB to generate physical address in case of cache miss
CPU
TLB
Page Tables
Physical Memory
Virtual Address
Miss
Invalid
Raise Exception
+
Offset
Hit
Physical Address
Data
Cache
Valid
Virtual Address
Miss
Hit
Virtual Cache

## Slide 40: Synonym
Definition: different virtual addresses mapped to same physical address
  Could be in same virtual address space or different virtual address spaces
  E.g., mmap() same file multiple times in same process or once in multiple processes
Aliasing problem: synonyms could be mapped to different locations in virtual cache
Typical solution: virtually-indexed-physically-tagged virtual cache
  Map synonyms to the same cache set (kernel ensures assigned VAs agree in index bits)
  Tag each virtual cache block by physical address
  Lookup virtual cache and TLB in parallel
  Update/invalidate other copies if physical address from TLB matches multiple entries
Synonym problem could affect any HW structure that deals with memory accesses
  E.g., load with synonym VA misses in store buffer if entries are tagged by VA and PID

## Slide 41: Putting it Together: Address Translation
Physical Page
PT Pointer
Page Table (1st Level)
Page Table (2nd Level)
V-P1 Index
Virtual Address
V-P2 Index
Offset
P-Page #
Offset
Physical Address

## Slide 42: Putting it Together: TLB
Physical Page
PT Pointer
Page Table (1st Level)
Page Table (2nd Level)
TLB
:
V-P1 Index
Virtual Address
V-P2 Index
Offset
P-Page #
Offset
Physical Address

## Slide 43: Putting it Together: Physical Cache
Physical Page
PT Pointer
Page Table (1st Level)
Page Table (2nd Level)
TLB
:
V-P1 Index
Virtual Address
V-P2 Index
Offset
P-Page #
Offset
Physical Address
Tag
Byte
Index
:
Tag
Block
Cache

## Slide 44: Putting it Together: Page Table, TLB, and Caches
CPU
Physical Memory
Virtual Address
Miss
Invalid
Raise Exception
+
Offset
Hit
Physical Address
Cache
Valid
Virtual Address
Miss
Hit
Virtual Cache
Physical Cache
Data
Hit
Physical Address
Miss
TLB
Page Tables

## Slide 45: Recall: Memory Hierarchy
Can TLB misses get resolved without ever going to main memory?
L3
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1
L1
L2
L2
Secondary Storage (SSD)
PT
Compiler
Managed
Hardware
Managed
Software
Managed (by OS)
Caching
TLB
TLB
PTE
PTE
PTE
PTE
PTE

## Slide 46: TLB Set Associativity
TLB hit time is added to all memory accesses
Should TLB be direct-mapped or have low associativity?
  No! TLB needs to have very few conflicts!
  Miss time is extremely high!
TLBs are typically fully-associative
  Significantly reduce conflict misses in return for slightly higher hit time
Average memory access time = hit-timeTLB + (miss-ratioTLB x miss-timeTLB)
CPU
TLB
Cache
Memory

## Slide 47: Do TLBs Always Improve Performance?
Example: for HD displays, video frame buffer could be large
  E.g., 4k display: 32 bits x 4K x 3K = 48MiB (spans12K of 4KiB pages)
Even large on-chip TLB with 256 entries cannot cover entire display
Each horizontal line of pixels could be on on page
Drawing vertical line could require loading a new TLB entry

## Slide 48: Superpages: Improving TLB Hit Rate
Reduce number of TLB entries for large, contiguous regions of memory
  Represent 2 adjacent 4KB pages by single 8KB superpage
By setting a flag, TLB entry can be a page or a supperpage
  E.g., in x86: 4KB (12 bits offset), 2MB (21 bits offset), or 1GB (30 bits offset)

## Slide 49: Linux Virtual Memory Map Prior to KPTI Patch
Address space of user process includes kernel memory
Kernel memory is protected from user process by owner bit
+ On system calls or interrupts, kernel page tables are always present
  Mitigating context-switch overheads (e.g., TLB flush, page-table swapping, etc.)
– It exposes serious security vulnerabilities that have been exploited by various attacks
  E.g. Meltdown and Spectre attacks
Empty
Space
Kernel Addresses
User Addresses
User
Addresses
Kernel Addresses
0x00000000
0xC0000000
0xFFFFFFFF
0x0000000000000000
0x00007FFFFFFFFFFF
0xFFFF800000000000
0xFFFFFFFFFFFFFFFF
128TiB
3GiB Total
1GiB
128TiB
32-Bit Virtual Address Space
64-Bit Virtual Address Space
Canonical Hole

## Slide 50: Meltdown Attack: Background
Branches can significantly slow down out-of-order execution
  E.g., processor has to wait for many cycles to determine direction of conditional jump
To speed up out-of-order execution, modern processors implement branch predictors (BP)
  BP predicts whether conditional branch will be taken before its execution
  Predictions are usually based on previous executions of the branch
  Processor executes next instructions speculatively
  On branch misprediction, processor rolls back speculatively-executed instructions
    Their results do not change architectural state

## Slide 51: Meltdown Attack
Meltdown was announced in 2018
It affects Intel x86, IBM Power, and some ARM processors
Kernel page-table isolation (KPTI) patch was released to mitigate Meltdown
  Without PCID tag in TLB, KPTI needs to flush TLB twice on syscall and interrupts (800% overhead!)
  Need at least kernel v4.14 which utilizes PCID tag in new HW to avoid flushing
char array[256 * 4096]; // Skip 4096 to avoid HW cache prefetch
flush_cache(array); // Make sure array is not cached
try { // catch and ignore SIGSEGV (illegal access)
char result = *(char *)kernel_address; // Segmentation fault
char dummy = array[result * 4096]; // Leak info!
} catch(){;} // Could use signal() to catch SIGSEGV
for (int i = 0; i < 256; i++)
if (is_in_cache(array[i * 4096]))
printf(“%d\n”); // found byte at kernel_address

## Slide 52: Summary
Principle of locality
  Programs access small portion of address space at any instant of time
Cache organizations
  Direct-mapped, set-associative, fully-associative
Three (+1) major categories of cache misses
  Compulsory, conflict, capacity, coherence
TLB: caching applied to address translations
  Cache relatively small number of PTEs
  Fully associative (since conflict misses expensive)
  On TLB miss, page table is traversed and if PTE is invalid, cause page fault
  On change in page table, TLB entries must be invalidated

## Slide 53: Questions?
globaldigitalcitizen.org

## Slide 54: Acknowledgment
Slides by courtesy of Anderson, Ousterhout, Sorin, Asanovic, Culler, Stoica, Silberschatz, Joseph, and Canny